## Slide 1
Alternating emf: Alternating emf is that emf which continuously changes in magnitude and periodically reverses its direction.
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
E, I – Instantaneous value of emf and current E0, I0 – Peak or maximum value or amplitude of emf and current
ω – Angular frequency t – Instantaneous timeωt – Phase
Symbol of AC Source
E = E0 sin ωt
Alternating Current: Alternating current is that current which continuously changes in magnitude and periodically reverses its direction.
I = I0 sin ωt

## Slide 2
Average or Mean Value of Alternating Current:
Average or Mean value of alternating current over half cycle is that steady current which will send the same amount of charge in a circuit in the time of half cycle as is sent by the given alternating current in the same circuit in the same time.
dq = I dt = I0 sin ωt dt
= =
Mean Value of AC, Im = Iav =
Im = Iav = 2 I0 / π = 0.637 I0 = 63.7 % I0
Average or Mean Value of Alternating emf:
Em = Eav = 2 E0 / π = 0.637 E0 = 63.7 % E0
Note: Average or Mean value of alternating current or emf is zero over a cycle as the + ve and – ve values get cancelled.

## Slide 3
Root Mean Square or Virtual or Effective Value of Alternating Current:
Root Mean Square (rms) value of alternating current is that steady current which would produce the same heat in a given resistance in a given time as is produced by the given alternating current in the same resistance in the same time.
dH = I2R dt = I02 R sin2 ωt dt
H = ∫ I02 R sin2 ωt dt
0
T
H = I02 RT / 2
If Iv be the virtual value of AC, then
Idc = Irms = Ieff = I0 / √2 = 0.707 I0 = 70.7 % I0
Root Mean Square or Virtual or Effective Value of Alternating emf:
Edc = Erms = Eeff = E0 / √2 = 0.707 E0 = 70.7 % E0
(After integration)
H = Idc 2 RT
Le dH be the heat produced in the resistance R in dt seconds when AC flowed through it, then

## Slide 4
A phasor (short for phase vector) is a rotating vector that represents a sinusoidal wave
(like an alternating voltage or current). At any instant it projection of either of the axes gives the instantaneous value
Phasor
In figure,
In figure, BC is the projection of on Y axis, which represents the instantaneous value E
Similarly , projection of on X axis gives
Cos

## Slide 5
AC Circuit with a Pure Resistor:
R
E = E0 sin ωt
E = E0 sin ωt
I = E / R
= (E0 / R) sin ωt
I = I0 sin ωt
(where I0 = E0 / R and R = E0 / I0)
Emf and current are in same phase.
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin ωt
E0
I0
ωt
y
x
0
Phasor Diagram.

## Slide 6
AC Circuit with a Pure Inductor:
L
E = E0 sin ωt
E = E0 sin ωt
Induced emf in the inductor is
In order to maintain the flow of current, the applied emf must be equal and opposite to the induced emf.
or,
I =
(where I0 = E0 / ωL and XL = ωL = E0 / I0) XL is Inductive Reactance. Its SI unit is ohm.
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin (ωt - π / 2)
Current lags behind emf by π/2 rad.
0
x
0
E0
ωt
I0
y
π/2
)

## Slide 7
AC Circuit with a Capacitor:
E = E0 sin ωt
(where and XC is Capacitive Reactance. Its SI unit is ohm.
y
E0
ωt
I0
π/2
x
0
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin (ωt + π / 2)
Current leads the emf by π/2 radians.
C

## Slide 8
Variation of XL with Frequency:
I0 = E0 / ωL and XL = ωL
XL is Inductive Reactance and ω = 2π f
XL = 2π f L i.e. XL α f
XL
f
0
Variation of XC with Frequency:
I0 = E0 / (1/ωC) and XC = 1 / ωC
XC is Capacitive Reactance and ω = 2π f
XC = 1 / 2π f C i.e. XC α 1 / f
XC
f
0
TIPS:
Inductance (L) can not decrease Direct Current. It can only decrease Alternating Current.
Capacitance (C) allows AC to flow through it but blocks DC.

## Slide 9
AC Circuit with L, C, R in Series Combination:
E = E0 sin ωt
C
L
R
VL
VC
VR
In R, current and voltage are in phase.
In L, current lags behind voltage by π/2
In C, current leads the voltage by π/2
VL - VC
VR
I
E
Φ
The applied emf appears as Voltage drops VR, VL and VC across R, L and C respectively.
=
VR
VL
VC
I
π/2
π/2
0
- VC
VL
VR
I
π/2
VC
=
=
=
=
* Z is called impedance
E =

## Slide 10
How phase changes across three LCR cases
tan Φ =
XL – XC
R
tan Φ =
ω L – 1/ωC
R
Special Cases:
Case I: When XL > XC i.e. ω L > 1/ωC,
tan Φ = +ve or Φ is +ve
The current lags behind the emf by phase angle Φ and the LCR circuit is inductance - dominated circuit.
Case II: When XL < XC i.e. ω L < 1/ωC,
tan Φ = -ve or Φ is -ve
The current leads the emf by phase angle Φ and the LCR circuit is capacitance - dominated circuit.
Case III: When XL = XC i.e. ω L = 1/ωC,
tan Φ = 0 or Φ is 0°
The current and the emf are in same phase. The impedance does not depend on the frequency of the applied emf. LCR circuit behaves like a purely resistive circuit.

## Slide 11
Resonance in AC Circuit with L, C, R:
When XL = XC i.e. ω L = 1/ωC, tan Φ = 0 or Φ is 0°
At resonant angular frequency ωr,
i.e. The impedance offered by the circuit is minimum and the current is maximum. This condition is called resonant condition of LCR circuit and the frequency is called resonant frequency.

## Slide 12
Band width = 2 ∆ ω
Quality factor (Q – factor) is defined as the ratio of resonant frequency to band width.
or Q = ωr L / R
or Q = 1 / ωrCR
Q = VL / VR
or Q = VC / VR
Resonant Curve & Q - Factor:
It can also be defined as the ratio of potential drop across either the inductance or the capacitance to the potential drop across the resistance.
ωr
I0max
ω
0
R1
R2
R3
I0
I0max / √2
ωr - ∆ ω
ωr + ∆ ω
R1 < R2 < R3
In figure, three plots with Vs of three different LCR circuits are given

## Slide 13
Power in AC Circuit with L, C, R:
Instantaneous Power = E I
=
E = E0 sin ωt
I = I0 sin (ωt + Φ) (where Φ is the phase angle between emf and current)
If the instantaneous power is assumed to be constant for an infinitesimally small time dt, then the work done is
dW = E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ]
Work done over a complete cycle is
W = E0I0 cos Φ x T / 2
Average Power over a cycle is Pav = W / T
(where cos Φ = R / Z
= R /√ [R2 + (ω L – 1/ωC)2] is called Power Factor)
Pav = Ev Iv cos Φ

## Slide 14
Power in AC Circuit with R:
In R, current and emf are in phase.
Φ = 0°
Pav = Ev Iv cos Φ = Ev Iv cos 0° = Ev Iv
Power in AC Circuit with L:
In L, current lags behind emf by π/2.
Φ = - π/2
Pav = Ev Iv cos (-π/2) = Ev Iv (0) = 0
Power in AC Circuit with C:
In C, current leads emf by π/2.
Φ = + π/2
Pav = Ev Iv cos (π/2) = Ev Iv (0) = 0
Pav = Ev Iv cos Φ
Wattless Current or Idle Current:
The component Iv cos Φ generates power with Ev.
However, the component Iv sin Φ does not contribute to power along Ev and hence power generated is zero. This component of current is called wattless or idle current.
P = Ev Iv sin Φ cos 90° = 0
Ev
Iv
Iv cos Φ
Iv sin Φ
Φ
90°

## Slide 15
Transformer:
Transformer is a device which converts lower alternating voltage at higher current into higher alternating voltage at lower current.
Principle:
Transformer is based on Mutual Induction.
It is the phenomenon of inducing emf in the secondary coil due to change in current in the primary coil and hence the change in magnetic flux in the secondary coil.
Theory:
(where K is called Transformation Ratio or Turns Ratio)
For an ideal transformer,
Output Power = Input Power
Efficiency (η):
For an ideal transformer η is 100%
S
Load
P

## Slide 16
Step - up Transformer:
Step - down Transformer:
Load
P
S
P
S
Load
NS > NP i.e. K > 1
ES > EP & IS < IP
NS < NP i.e. K < 1
ES < EP & IS > IP
Energy Losses in a Transformer:
Copper Loss: Heat is produced due to the resistance of the copper windings of Primary and Secondary coils when current flows through them.
This can be avoided by using thick wires for winding.
Flux Loss: In actual transformer coupling between Primary and Secondary coil is not perfect. So, a certain amount of magnetic flux is wasted.
Linking can be maximized by winding the coils over one another.

## Slide 17
Iron Losses:
a) Eddy Currents Losses:
When a changing magnetic flux is linked with the iron core, eddy currents are set up which in turn produce heat and energy is wasted. Eddy currents are reduced by using laminated core instead of a solid iron block because in laminated core the eddy currents are confined with in the lamination and they do not get added up to produce larger current. In other words their paths are broken instead of continuous ones.
Solid Core
Laminated Core
b) Hysteresis Loss:
When alternating current is passed, the iron core is magnetized and demagnetized repeatedly over the cycles and some energy is being lost in the process. This can be minimized by using suitable material with thin hysteresis loop.
Losses due to vibration of core: Some electrical energy is lost in the form of mechanical energy due to vibration of the core and humming noise due to magnetostriction effect.